## Slide 1: Presentation 30:
STARTING 3-TAB SHINGLES

## Slide 2: Underlayment
Felt underlayment is installed on a roof deck before shingles are applied.

## Slide 3: Underlayment
It comes in rolls three feet wide.
It is installed with an overlap.
4″ minimum
2″ minimum

## Slide 4: Drip Edge
Metal drip edge is often installed to protect the roof perimeter.

## Slide 5: Drip Edge
This comes in lengths of ten feet.

## Slide 6: Shingles
3-tab shingles are typically 1′ x 3′.
12″
36″
Cutout slots
Self-Sealing Strip
Typical Nail Locations
Attributes of a shingle:

## Slide 7: Starters
Starter course must be installed to seal the tabs along the perimeter of the roof.

## Slide 8: Starters
Starter course is a full shingle with the tabs cut off.

## Slide 9: Starters
Starter course is a full shingle with the tabs cut off.

## Slide 10: Starters
It is placed under the first course.
Starter also fills in the back of the cutout slots.

## Slide 11: Starters
Notice the self-sealing strip under the tab.

## Slide 12: Beginning Shingles
Install the starter strip on roof perimeter.
NOTE:
Self-Sealing strip along the roof edge.
Rake edge is installed first.

## Slide 13: Beginning Shingles
Install the starter strip on roof perimeter.
NOTE:
Self-Sealing strip along the roof edge.
Rake edge is installed first.
Starter and first shingle butt seams do not line up.

## Slide 14: Beginning Shingles
To speed up installation, the first piece of each course is cut ½ tab shorter than the previous course.

## Slide 15: Full Shingle Installation
Full shingles are now installed across the roof, but in a vertical pattern.
A full shingle completes a course.
Then another set of starter pieces is installed.

## Slide 16: Full Shingle Installation
The roof is completed in a similar fashion.
Top course is cut off.

## Slide 17: Full Shingle Installation
Waste pieces from making the ½ tab starters are used to complete the roof.
Once a full shingle.

## Slide 18: Conclusions
Underlayment is the first step in installing shingles.
Drip edge gives strength to the roof edge.
Starter course is a full shingle with the tabs cut off.
Self-sealing strip is close to roof edge.
Each course is started with ½ tab removed.
Waste pieces from the ½ tab cutoffs are used to complete the roof.